## Slide 1
Title & Team Members
Smart Home Security &
Automation System
IoT
Face Recognition
Fire Detection
Climate Control
Remote Monitoring
Zewail City of Science and Technology
CIE Program Â· Embedded Systems Exhibition
June 29, 2026
TEAM:
TM1
Team Member 1
TM2
Team Member 2
TM3
Team Member 3
SV
Supervisor
Research Problem / Context
The Challenge
Traditional home security relies on static credentials â€” keys, PINs, and passwords â€” that are easily lost, shared, or duplicated. These systems operate in isolation with no real-time awareness of environmental threats.
No biometric identification â€” anyone with a key can enter
No fire or environmental hazard detection
Zero remote visibility â€” homeowners are uninformed during critical events
Manual climate control wastes energy with no intelligent feedback
Separate disconnected devices instead of one unified system
Research Question
"How can we build a unified, low-cost embedded system integrating biometric access, environmental sensing, and remote monitoring in a reliable standalone architecture?"
Research Methodology
System Design Approach
A dual-microcontroller architecture was selected to separate computer vision from control logic, ensuring reliable operation even when network connectivity is unavailable.
1
Requirements Analysis
Identified 8 functional requirements: face access, motion-triggered capture, gas detection, fire alert, climate control, lighting, remote monitoring, reliable power.
2
Hardware Selection
ESP32 main controller + ESP32-CAM for on-device face rec. PIR wired directly to ESP32-CAM GPIO for wake-on-motion. MQ-2 gas sensor added.
3
Architecture Decision
ESP-NOW chosen for board-to-board comms â€” no WiFi dependency, low latency, reliable at exhibition.
4
Circuit Design
2N2222 transistor driver for DC fan, 1N4007 flyback diode, 4.7kΩ DHT22 pull-up, 330Ω LED resistors.
5
Software & Integration
Blynk IoT dashboard (V0–V8) for remote control. Face rec runs entirely on-device — no cloud API.
Key Findings
What We Discovered
âœ“
On-device Face Recognition
ESP32-CAM processes biometric data locally â€” no cloud API latency, no privacy risk, works offline.
âœ“
ESP-NOW Reliability
Wireless board-to-board comms proven stable â€” no WiFi dependency, works reliably at exhibition venues.
âœ“
Single 5V Supply Works
All components powered from one DC adapter with shared ground â€” clean, stable, exhibition-ready.
âœ“
Blynk Dashboard Complete
8 virtual pins cover full control: LEDs, lock, buzzer, gas, temp, humidity, face alert, PIR status.
âœ“
Auto Climate Control
DHT22 threshold logic (>30°C) activates fan driver circuit â€” tested stable across 2-hour runtime.
âœ“
Multi-Hazard Detection
Flame sensor + MQ-2 gas sensor provide fire, smoke, and LPG leak alerts with buzzer + Blynk notification.
Solution / Prototype
System Operation
PIR Sensor
Motion Detected
ESP32-CAM
Camera Triggered
Face Recognition
On-Device Processing
Known Person?
KNOWN PERSON
ESP-NOW
â†’
ESP32
â†’
Servo Opens Door
Inside LEDs ON
UNKNOWN PERSON
Capture Photo
â†’
Upload to
Blynk
â†’ Phone Notification
YES
NO
GPIO 12 Servo Â· GPIO 14 Flame Â· GPIO 15 Fan Â· GPIO 27 Gas
GPIO 25 DHT22 Â· GPIO 26,33 LEDs Â· GPIO 4 Outside LED Â· GPIO 32 Buzzer
Impact / Application
Outcomes & Future Scope
2
MCUs
8
Sensors &
Actuators
5V
Single
Supply
UART
Reliable
Comms
Achievements
Keyless personalized door access via on-device face recognition
PIR auto-lighting improves energy efficiency and perimeter security
Temperature-controlled fan maintains indoor comfort automatically
Flame sensor provides early fire detection with audible alarm
Full remote monitoring & control via Blynk smartphone dashboard
Reliable dual-board architecture operates without internet
Future Work
Reed switch for physical door-state confirmation
Multi-face enrollment via SD card database
Gas / CO sensor for multi-hazard detection
OTA firmware updates over WiFi
Replace Blynk with local MQTT broker
Scalable â€” spare GPIOs ready for expansion
Smart Home Security & Automation System Â· CIE Program Â· Zewail City of Science and Technology
Embedded Systems Exhibition Â· June 29, 2026